## Slide 1: NGTP Overview

## Slide 2: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 3: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 4
Design pattern, framework, solution,…
Standard building blocks
Standard interfaces
Reusability
Easy integration of legacy systems
Easy integration of new systems
Current version: 2.0 (?)
Next Generation Telematics Pattern
Overview

## Slide 5
Overview (cont.)

## Slide 6: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 7
Building blocks
Telematics Unit
Integrated within vehicle
Mobile phone
Out side of NGTP backend
Establish/accept connection with/from DSPT
Send/receive/handle data to/from DSPT
Bearers independent (SMS, WLAN,…)
Messages are uplink (MO)

## Slide 8
Dispatcher
Handle HEADER of NGTP message only
Dispatch messages to other components
Send messages from other components to TU
Able to handle of both voice and data messages
Able to switch bearer (SMS, WLAN,…)
Messages are downlink (MT)
Multiple protocols: UDP, HTTP/HTTPS (over TCP), SMS
Resending mechanism stop after receiving DSPT ACK
Encryption/decryption of messages
Building blocks (cont.)

## Slide 9
Building blocks (cont.)
Handle SERVICE DATA of NGTP message
Data conversion (from/to DSPT to/from SI)
Support multiple data formats
Forward data to SI/DSPT
Service Handler

## Slide 10
Building blocks (cont.)
Data hub of other components (PSAP, CC, OS, CP)
Send service data (APP ACK) to TU (via SH & DSPT)
Service Integrator

## Slide 11
Building blocks (cont.)
Public Safety Answering Point
Emergency calls call center
Region dedicated (dispatcher to current location PSAP)

## Slide 12
Building blocks (cont.)
Call Center
Deliver vocal data to TU (POI, phone number,…)
Receive data from TU (POI,…)
Connection can be direct between DSPT & CC to reduce latency

## Slide 13
Building blocks (cont.)
Other Services
Any kind of services can connect to NGTP backend (hotel booking,…)

## Slide 14
Building blocks (cont.)
Provisioning Data Provider
  Keep DSPT flexible by holding provisioned (by OEM, TU manufacturer) data
  How to reach the TU (IP-address, IMSI)
  Encryption (algorithm to use, keys)
  Latest channel used by the TU (UDP, SMS,...)
  Which component to trigger on incoming messages

## Slide 15
Building blocks (cont.)
Custom Data Provider
  Keep customer & vehicle related data relevant for a service
  Independent from services (different services can reuse same data from CDP)

## Slide 16
Building blocks (cont.)
Content Provider
  Content dispatcher (query content from other sources depends on request from TU)
  Content includes: POI, weather forecast, traffic fules,...
  Can hold online or offline (in database) content

## Slide 17: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 18
Design & communication concepts
Design
  Event
  …
Communication
  Trigger
  Operation

## Slide 19
Design & communication concepts
(cont.)
Communication
Uni-directional (except IF#1 & IF#8)
Trigger
Originated from DSPT only (to other higher components in NGTP stack)
Unique by Event
Operation
Or method (from programming/technical point of view)
Provided/implemented by interfaces (later)
Call by some to retrieve info from others after receiving
Trigger

## Slide 20
Design & communication concepts
(cont.)
Design
Event
A use case, for e.g.: User (TU) establish an emergency call, or NGTP backend establish an update request to software @ TU side,…
Defined by an unique ID (later)
Multiple message can belong to same event

## Slide 21: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 22
Interfaces
Define operations
Operations are services (methods, APIs) provided by lower level to higher level components within NGTP stack
Naming convention (name indicates direction from low to high component)
Mostly uni-directional

## Slide 23
Interfaces (cont.)
Focus on this only (later)

## Slide 24: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 25
General aspects
Aspects need to be considered when design a telematics system obeys NGTP principles
Just guidelines & recommendations
Security
Secured communication channel like SSL
End-to-end data encryption
Authentication
…
Logging
Timestamp
Event ID
Distributed logging
Centralized logging
…
Monitoring
Failure detection
Diagnosis of issues
…

## Slide 26: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 27
TSDP
A name given by WirelessCar (WC) for its implementation of NGTP infrastructure
Telematics Services Delivery Platform
Components and their roles are as same as described in previous sections
Plus other components

## Slide 28
TSDP (cont.)
Voice Gateway
Allocate & store phone numbers for e-call, b-call (CRQNs – Call Request Numbers)
Decide & forward CRQNs to DSPT that send back for TU to use

## Slide 29
TSDP (cont.)
Master Data Service
Add & store vehicle profile, TU profile
Vehicle profile added by JLR system
TU profile added by LGE
Vehicle profile & TU profile will be connected (programmatically) when running provisioning application (FT) within VDC

## Slide 30: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 31
LGE NGTP service
Focus on this only (later)
As said earlier…

## Slide 32
Handle HEADER of NGTP message only
Dispatch messages to other components
Send messages from other components to TU
Able to handle of both voice and data messages
Able to switch bearer (SMS, WLAN,…)
Messages are downlink (MT)
Multiple protocols: UDP, HTTP/HTTPS (over TCP), SMS
Resending mechanism stop after receiving DSPT ACK
Encryption/decryption of messages
LGE NGTP service (cont.)
Dispatcher
LGE NGTP service resides in here
As said earlier…

## Slide 33
Handle HEADER of NGTP message only
Dispatch messages to other components
Send messages from other components to TU
Able to handle of both voice and data messages
Able to switch bearer (SMS, WLAN,…)
Messages are downlink (MT)
Multiple protocols: UDP, HTTP/HTTPS (over TCP), SMS
Resending mechanism stop after receiving DSPT ACK
Encryption/decryption of messages
LGE NGTP service (cont.)
WC Dispatcher
LGE NGTP service resides in here
That means:
Handle HEADER of NGTP message only
Dispatch messages to other components (applications within TU that sent corresponding message)
Send messages from other components (applications within TU) to DSPT
Able to handle of both voice and data messages
Able to switch bearer (SMS, WLAN,…)
Messages are uplink (MO)
Multiple protocols: UDP, HTTP/HTTPS (over TCP), SMS
Resending mechanism stop after receiving DSPT ACK
Encryption/decryption of messages
And many more that specific to JLR requirements…

## Slide 34
LGE NGTP service (cont.)
LGE NGTP service
resides in here
SVC CODEC
DSPT CODEC
Component defines structure/format for SERVICE section of a NGTP message
Know how to encode/decode that section
Provided by 3rd party (later)
Component defines structure/format for HEADER section of a NGTP message
Know how to encode/decode that section
Provided by 3rd party (later)

## Slide 35
LGE NGTP service (cont.)
What’s about data encryption?
What’s about data communication over the Internet?
© Image courtesy of Google Images

## Slide 36
LGE NGTP service (cont.)
In summary
App (service)
App (service)
App (service)
Its own logic
CURL
OpenSSL
SVC & DSPT CODEC
NGTP service
TU (JLR VDC)
IF#1
WC DSPT

## Slide 37: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 38
Vehicle interface
A.K.A IF#1
Bi-directional
Located @ NGTP backend
Vehicle profile added by JLR system
TU profile added by LGE
Vehicle profile & TU profile will be connected (programmatically) when running provisioning application within VDC

## Slide 39
Vehicle interface (cont.)

## Slide 40: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 41
Vehicle interface (cont.)
ASN.1
IF#1 uses ASN.1. to (recursively) define structure of a NGTP message
  Name
  Type
  Length
  …
Tools to generate ASN.1 format to difference programming language
https://www.oss.com/asn1/products/asn1-cpp/asn1-cpp.html

## Slide 42
Vehicle interface (cont.)
ASN.1 (cont.)
https://www.oss.com/asn1/products/asn1-cpp/asn1-cpp.html
ASN.1 Compiler

## Slide 43
Vehicle interface (cont.)
ASN.1 (cont.)
https://www.oss.com/asn1/products/asn1-cpp/asn1-cpp.html
ASN.1 Compiler
Specified by JLR
Discuss with LGE & WC
Provided by OSS NOKALVA, INC.
SVC CODEC said earlier

## Slide 44
Vehicle interface (cont.)
ASN.1 (cont.)
https://www.oss.com/asn1/products/asn1-cpp/asn1-cpp.html
Provided by OSS NOKALVA, INC.
DSPT CODEC said earlier

## Slide 45
Vehicle interface (cont.)
ASN.1 (cont.)
https://www.oss.com/asn1/products/asn1-cpp/asn1-cpp.html
Hierarchical structure
Encoding/decoding, printing, error handling,…

## Slide 46: Agenda
Overview
Building blocks
Design & communication concepts
Interfaces
General aspects
TSDP
LGE NGTP services
Vehicle interface
  ASN.1
  NGTP messages

## Slide 47
NGTP Message
Defined by ASN.1 notation
Packed Encoding Rules Unaligned (PER/U) is used for binary encoding of payload data
  Efficiently minimizing payload data
  Low TU resource requirements
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable

## Slide 48
NGTP Message (cont.)
Defined by ASN.1 notation
Packed Encoding Rules Unaligned (PER/U) is used for binary encoding of payload data
  Efficiently minimizing payload data
  Low TU resource requirements
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable

## Slide 49
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DDU
To retrieve crypto key from the PDP (together with the data in the security context)
To be able to throw away ”old” messages without having to decrypt the full message.
NGTPDispatcherDataUnencrypted ::= SEQUENCE {
messageCreationTime TimeStamp,
messageTimeToLive INTEGER(0..2047),
msgCounter MessageCounter,
vehicleIdentification VehicleIdentification
}

## Slide 50
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DDU – Message Creation Time
-- Time when this message was created by the dispatcher part creator.
-- The sender must ensure that a timestamp is never reused for a specific car
messageCreationTime TimeStamp, --41bit
TimeStamp ::= SEQUENCE {
seconds INTEGER(0..2147483647), -- UTC seconds since January 1st, 2000, 00:00 (31 Bit)
millis INTEGER(0..999) OPTIONAL -- Millisecond within the second
}
It is very important that the message creation time is not reused for a specific vehicle.
This is so because the dispatcher will not pass on a message having the same message creation time as a message it has already processed.
Also very important because the security of the encryption requires the initialization vector (IV) to be unique (per encryption key), and the message creation time is part of the IV.

## Slide 51
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DDU – Message Time To Live
messageTimeToLive INTEGER(0..2047), --In steps of 10s. 0=no limit
Configurable by service type. E.g. an e-call should have longer TTL than others

## Slide 52
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DDU – Message Counter
-- The message counter is incremented for each new message sent, except for the
-- Dispatcher Ack where the received message counter is returned.
-- Each side has its own message counter
msgCounter MessageCounter,
MessageCounter ::= SEQUENCE {
uplinkCount INTEGER (0..255),
downlinkCount INTEGER (0..255)
}
Used to correlate requests and ACKs.
When the TU sends a new message, the uplinkCount should be increased.
When TSP sends a new message, the downlinkCount should be increased.
When TSP sends an app ack to TU, the uplinkCount should have the same value as the message that is acknowledged.

## Slide 53
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DDU – Message Counter (cont.)
  DsptAck – I have received your message and stored it reliably. It will be processed sometime in the future (normally within milliseconds). The DsptAck is sent from the Dispatcher.
  AppAck – I have received your message and fully processed it. The AppAck is sent from the implementing Domain Service.
From an application point-of-view the meaning of Application Acknowledgement(AppAck) and Dispatcher Acknowledgement (DsptAck) can be described like this:
Both are configurable in NGTP message: AppAckRequired (Boolean), DsptAckRequired (Boolean)

## Slide 54
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DDU – Vehicle Identification
--This field is added here to make it possible to identify the sender
--even for an encrypted message over a public APN.
vehicleIdentification VehicleIdentification
VehicleIdentification ::= CHOICE {
vin VIN,
--driveID can be used as an “anonymous” identifier. Currently not used.
driveID PrintableString (SIZE(17)),
--Generic equipment id. Used if provisioned by TSP.
equipmentId INTEGER(0..4294967295),
--Equipment serial number
equipmentSerial PrintableString (SIZE(10..20))
}
EquipmentSerial is used when performing a factory test (FT). VIN included in the service data.
TSP generates an equiment ID for a vehicle from the VIN when running FT.
The equipment ID is sent back to TU in the FT process.
The equipment ID is always used between the TU and the dispatcher after the FT has been performed.
The PDP holds a mapping equipment ID  VIN.
VIN is used in the rest of the TSDP stack.

## Slide 55
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD
Can be of three types
  Uplink
  Downlink
  Control
NGTPDispatcherData ::= CHOICE {
uplink UplinkNGTPDispatcherData, -- for ServiceDataMessages
downlink DownlinkNGTPDispatcherData,-- for ServiceDataMessages
control ControlNGTPDispatcherData -- for both downlink and uplink
}

## Slide 56
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Each message type consists of a common part (included in all types) and one specific part.
UplinkNGTPDispatcherData ::= SEQUENCE {
common NGTPDispatcherDataCommon,
extension UplinkNGTPDispatcherDataExtension
}
DownlinkNGTPDispatcherData ::= SEQUENCE {
common NGTPDispatcherDataCommon,
extension DownlinkNGTPDispatcherDataExtension
}
ControlNGTPDispatcherData ::= SEQUENCE {
common NGTPDispatcherDataCommon,
extension ControlNGTPDispatcherDataExtension
}

## Slide 57
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Each message type consists of a common part (included in all types) and one specific part.
UplinkNGTPDispatcherData ::= SEQUENCE {
common NGTPDispatcherDataCommon,
extension UplinkNGTPDispatcherDataExtension
}
DownlinkNGTPDispatcherData ::= SEQUENCE {
common NGTPDispatcherDataCommon,
extension DownlinkNGTPDispatcherDataExtension
}
ControlNGTPDispatcherData ::= SEQUENCE {
common NGTPDispatcherDataCommon,
extension ControlNGTPDispatcherDataExtension
}
NGTPDispatcherDataCommon ::= SEQUENCE {
eventInitiator EventInitiator,
eventCreationTime TimeStamp,
serviceType INTEGER (0..255),
messageType DSPTMessageType,
dsptAckRequired BOOLEAN,
statelessNGTPmessage BOOLEAN,
...
}

## Slide 58
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Common – Even Initiator
--Where was the event started eventInitiator EventInitiator, --1
bitEventInitiator ::= ENUMERATED {
tu (0),
backend (1)
}
Should indicate if the message was created by the TU (bit set to 0) or by the TSP (bit set to 1).

## Slide 59
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Common – Even Creation Time
eventCreationTime TimeStamp,
Timestamp indicating when the event that the message belongs to was created.
All messages belonging to the same event should have the same eventCreationTime.
Messages belonging to different events must have different messageCreationTimes.
The dispatcher uses the eventCreationTime to find out which event a message belongs to.

## Slide 60
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Common – Service Type
-- A value from ApplicationServiceType in separate ---- asn.1 file
serviceType INTEGER (0..255),
From TU (JLR TCU) point of view, services are applications run above (and therefore use) NGTP service’s APIs
Passed on from the dispatcher to the SH
Service Name | Value
ECALL | 1
BCALL | 5
SVT | 15
… | …

## Slide 61
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Common – Message Type
messageType DSPTMessageType
DSPTMessageType ::= ENUMERATED {
...
upServiceData (2),
downServiceData (3),
dsptAck (4),
...
-- 11 to 31 is reserved

## Slide 62
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Common – Dispatcher Ack Required
dsptAckRequired BOOLEAN,
Determines if a dispatcher ACK should be sent in response to this message.

## Slide 63
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Common – Stateless NGTP Message
-- statelessNGTPmessage TRUE is used in a message not -- expecting any response.
statelessNGTPmessage BOOLEAN,
Stateless
Does not expect for response
Will be forgotten when received DSPT ACK
Stateful
Expect for response
Ended when either side (TU or DSPT) sends Terminate message
Those are called communication flow
4 types in total (TU <-> DSPT)

## Slide 64
NGTP Message (cont.)
Section | Transport header | Message header | Dispatcher Data Unencrypted | Dispatcher Data | Dispatcher Signature | Service Data | Message Signature
Size (bytes) | 3 | 5 | Variable | Variable | Variable | Variable | Variable
DD (cont.)
Let come back to Event
Event
A use case, for e.g.: User (TU) establish an emergency call, or NGTP backend establish an update request to software @ TU side,…
Defined by an unique ID (later)
Multiple message can belong to same event
In JLR VDC – WC NGTP, I think Event is combination of what already mentioned in NGTPDispatcherDataCommon(DD) + Equipment ID (DDU)

## Slide 65
Others need to be investigated
Transport support within NGTP service & DSPT (NGTP backend)
  UDP
  HTTP/HTTPS (over TCP)
  ...
Retry mechanism
Messages fragmentation and resemblance
Security (encryption & decryption of a NGTP message)
...